## Slide 1: ICC iMES Plan
2011/08/26

## Slide 2: ICC IMES Deploy Schedule

## Slide 3: Preparation Check Item –Infrastructure
AP Server 加入FIS或OA 域?
  加FIS 域
  ImportUser can’t import IES/ICCXXXX account ?
  要建Local 帳, update Account table ，預設密碼:123456
  Label Template Editor
    提示輸入user password
    IE need change configure
測試環境 -- ok
  DB /AP
  Edits server -- IEC Lee, Frank/家有
    SumatraPDF.exe /PrintPDF.js/PrintPDF.bat
產線環境 -- 安排時間先搬FIS DB,在整理DB Server
  DB Cluster
    SAN storage 重新分割 Qry Lun
      SQL_Init 30G/SQL_Data_ldf (100G)/SQL_Data_ndf(500G)/SQL_Backup(350G)
  AP NLB
  Backup DB
  Report DB
管理環境 --
  Mantis/SVN system

## Slide 4: Preparation Check Item – Installation
測試環境
  DB Schema 建置
    HPIMES
    HPEDI
    HPDocking
    GetData
    RBPC4Net
    LabelTemplateDB
  GetData DB Replicate Production BOM
    After replication completed need build trigger
  AP iMES Install
    RBPC
    LabelTemplate
    SA/FA/PAK/RCTO/Docking
    Portal Web
  Edits Install
產線環境
  DB Cluster failover 測試
  Cluster MSDTC測試
  DB Schema 建置
  iMES installation
  Edits installation

## Slide 5: Preparation Check Item – Business Logical
Confirm SA/FA/PAK Process flow
轉資料SP
  設置資料
  資料
標籤格式內容
編碼規則
SMT
  SMT MO 管控(CQ 无)
PCA -- Vic
  QC 流程（15站完成后，送给QC验机器，并记录。IMES 系统有组LOT一系列流程）
  CQ无 PCA Cosmetics 站别（IMES流程图上有此功能）
FA -- Frank
  收集Thermal 在MB input 站（IMES 独立站）
  CQ : Image 先down --->RUN in
  CQ 无PIA 流程
  Light Guid CQ在PAK贴标签 ,IMES 在FA 贴标签
  Function 测试站 CQ 只有PRE TEST( IMES 系统有pre test ,AFT test,Run in test.CQ 在run in 时会开无线，然后把结果上传 FIS.)
PAK -- Benson
  CQ 有主上主下标签check 界面（此站在COA站下一站），IMES 无。
  POD 打印 混线生产，称重站需要分2种标签（连接2台printer）。
  CQ BT 流程在COA 打印BT 標籤，然后在Combine DN for BT 时打印COO Label。（IMES 系统不论是BT或者非BT都是在kitting6打印COO label）

## Slide 6: HW Infrastructure

## Slide 7: HW Information

## Slide 8: iMES Infrastructure—Production Environment
Migrate DB Server*2
  DL580 4* 8 core/64 G MEM *2 台
  SAN 500G / 1T * 2 drivers
  Windows 2008 R2 & SQL Server 2008 R2+SP1
  DB Cluster
    HP Cluster node1
    TSB Cluster node2
  加入FIS 域
SAN Storage Split Lun for DB
  At least three Luns, Capacity 2T
  One Lun master DB, second Lun data & Temp DB, Third Lun is for log file
Backup Server *1
  DL370 Server Disk Array
  DB log shipping
Report Server*1
  DL370 Server Disk Array
  DB log shipping
遷移目前FIS DB 至新的DB server DL580 server
  需要跟user 確認時間
準備AP Server *2 for HP
  Windows 2008 R2
  Dot Net Framework v3.5 以上
  Office excel component
  Zebra 打印驅動
  AP Server 需要有雙網卡
    FIS網段
    OA網段
    加入 OA 域
Edits Server
  Windows 2008 R2, .net framework v3.5
  FIS 域
DNS Server set up new server name mapping ip
Server時間同步

## Slide 9: iMES Infrastructure—Test Environment
Test Server
  One DL370 Server , Raid 5 Disk Array
  Create Four VMs machine
    DB server
    AP Server *2
    Edits Server *1
  AP Server 需要有雙網卡
    FIS網段
    OA網段
    加入 OA 域
Install iMES
  DB schema
    HPIMES
    HPEDI
    GetData
    HPLabelTemplate
    HPRBPC4Net
  Replicate PE BOM DB to GetData DB
    Replicate BOM SP
  DB Job
  iMES AP Server
    SA/FA/PAK/RCTO/Query/Maintain service
    RBPC
    Label Template
    Portal
Install Mantis system for trace issue
  PHP server
  mySQL DB
Install Subversion system

## Slide 10: IMES Installation

## Slide 11: iMES Production Readiness
DB schema
  HPIMES
  HPEDI
  GetData
  HPLabelTemplate
  HPRBPC4Net
Replicate PE BOM DB to GetData DB
  Replicate BOM SP
  PE 直接在 iMES.GetData 建BOM,不須Replicate
DB Job
iMES AP Service
  SA/FA/PAK/RCTO/Query/Maintain service
  RBPC
  Label Template & Web
  Portal web

## Slide 12: IMES Data Model

## Slide 13: iMES Data Modelling
FIS Configure Data 遷移至 iMES DB
FIS Data遷移至 iMES DB
BOM
  Replication
Process flow
  Confirm Process Station & flow
    Draw Process flow diagram
  Configure Process flow
    Line
    Station
    Process
Label Template
  Confirm print Template
    SA
    FA
    PAK
    RCTO
SA
FA
PAK
RCTO

## Slide 14: IMES Test Plan

## Slide 15: iMES Test Plan
SA
FA
PAK
RCTO

## Slide 16: IMES New Requirement

## Slide 17: iMES Modify Requirement

## Slide 18: IMES Training Plan

## Slide 20
Thank You
Question and Answer